## Slide 1: Biosolids Regulatory Framework Presented to CASA Members March 7, 2022
Greg Kester
gkester@casaweb.org
916-844-5262

## Slide 2: What will be covered
California Biosolids Management, Challenges, and Opportunities
Climate Change Mitigation Legislation
Biosolids Regulatory Foundation and Requirements
Research and Collaborative Studies
Summary and Conclusions

## Slide 3: California Biosolids Management in 2020
Chart: 
| Land Application | Landfill ADC | Landfill Disposal | Incineration | Surface Disposal | Deep Well Injection | Storage
2021 Biosolids (658,000 DMT) | 0.67021 | 0.11246 | 0.1155 | 0.022796 | 0.030395 | 0.013678 | 0.034954
Total Generated: 658,000 Dry Metric Tons (DMT)
  Land Application: 441,000
  Landfill: 150,000
    74,000 ADC
    76,000 Burial
  Incinerate: 15,000
  Surface Disposal: 20,000
  Deep Well Injection: 9,000
  Storage, long-term treatment: 23,000

## Slide 4: CA Legislation to Mitigate Climate Change
Achieve 40% reduction in GHG emissions below 1990 levels by 2030 and Carbon Neutrality by 2045
100% Clean/Renewable Electrical Energy by 2045 (with 50% by 2026 and 60% by 2030)
20% reduction in Carbon Intensity of transportation fuel by 2030
Short-Lived Climate Pollutant Reduction – 40% methane reduction by 2030 from 2013 (through SB 1383 implementation)
Healthy Soils Initiative, Natural & Working Lands Climate Smart Strategy, and Wildfire & Forest Resilience Action Plan

## Slide 5: SB 1383 Adopted in 2016 – Regulations Approved in 2020
Reduce Short-Lived Climate Pollutants
Legislation Adopted in 2016 and requires
  40% reduction in methane emissions with 2013 as the baseline by 2030
  75% organics diversion from landfills (including biosolids) relative to 2014 levels by 2025

## Slide 6: SB 1383 Implementation
We believe the state recognizes that Wastewater Sector is key to successful implementation
To that end, two incentives were included in regulations intended to create markets
  Disallow local ordinances that unreasonably restrict or prohibit land application of biosolids
  Every jurisdiction required to divert organic waste must then procure a product of that diversion  compost and/or beneficial use of biogas

## Slide 7: Opportunities Offered by the Wastewater Sector to Meet SB 1383 Objectives via Co-Digestion
Use of existing infrastructure to accept at least 75% of food waste currently landfilled for anaerobic digestion
Increase biogas production to generate renewable energy, low carbon transportation fuel, and pipeline grade RNG, in turn decreasing greenhouse gas emissions
Build healthy soils, sequester carbon, and reduce fossil fuel based inorganic fertilizer use through land application of biosolids
Develop collaborative partnerships with private sector

## Slide 8: Co-digestion Accelerates Diversion of Organics from Landfills
Opportunity:
~150 wastewater plants already utilize anaerobic digestion and have excess capacity - ~ 90+% of wastewater flow
  Plants are often located in urban areas near waste generation –> shorter haul
Challenges/Needs:
Must build partnerships with solid waste sector to maximize effective diversion
Cleanliness of organic waste stream must be assured (whether for co-digestion, digestion, or compost)
Markets must be assured for both biogas and biosolids

## Slide 9: Significant Additional Renewable Energy Potential
If co-digestion is maximized to utilize all existing capacity and 3.4 million tons of food waste is accepted we can increase energy by:
822,800 MegaWatt hours
7.5 million MBTu’s
71.4 Million Diesel Gallon Equivalents transportation fuel – when combined with what is produced from sewage sludge digestion - would allow 575 million miles to be driven by Heavy Duty Trucks with Renewable Fuel
Working with CARB to ensure heavy duty trucks, vactor trucks, etc. can continue to use our RNG!
Electric options don’t exist yet and won’t for some time

## Slide 10: Further Opportunities for the Water Sector
CPUC on 2/24 adopted a decision to require Investor Owned Utilities (IOUs) to procure biomethane via pipeline injection
POTWs who co-digest will be given priority as targeted customers
------
CEC contacted CASA to see how the water sector might help address potential energy shortfall
Working with them on opportunities to go off grid during peak demand via storage reservoir pumping shifts, co-gen, & battery storage – operational changes and worker schedule shifts possible

## Slide 11: Further Opportunities for the Water Sector
Need capital, tariff changes, policy shifts, regulatory relief to execute
Positive work continues with Vice Chair Gunda, Commissioner Douglas and their teams
Many Thanks to Robb Grantham – Rancho California for his leadership on our behalf
-----
Working with CNRA to include biosolids land application in the Natural and Working Lands program

## Slide 12: Biosolids Challenges in California
Rural/Urban disparity – most production in coastal urban centers, largest need in Central Valley and other rural agricultural centers
Poor management (refusal to fix roads, be good neighbors, etc.) and oversight in early 1990’s resulted in restrictive ordinances – both are no longer an issue and no new ordinances since 2007
Kern and Imperial County Prohibitive ordinances were challenged in court and overturned
SB 1383 regulations disallow restrictive or prohibitive ordinances on biosolids land application

## Slide 13: Biosolids Challenges in California
Very limited options for renewable resource which will increase as long as society exists
Incineration (only 1 and do not expect any more in CA)
Surface Disposal (only 5 and do not expect any more)
Alternative Daily Cover or disposal in Landfills (98 send at least some for this purpose but ~0 as of 2025)
LAND APPLICATION – Best sustainable option in long-term

## Slide 14: Biosolids Land Application in California - 2020
AZ
NEVADA
MEXICO
County Ordinance Requirements and Biosolids Bans
Ban on All Land Application
Ban on Class B
Conditional Use Permit Required
Class B Land Application Allowed
No Regulations/Ordinances Enacted
HUMBOLDT
DEL NORTE
MENDOCINO
SAN FRANCISCO
SF
SISKIYOU
MODOC
LASSEN
SHASTA
TRINITY
HUMBOLDT
DEL NORTE
MENDOCINO
TEHAMA
PLUMAS
GLENN
BUTTE
SIERRA
NEVADA
PLACER
EL DORADO
ALPINE
AMADOR
COLUSA
LAKE
SONOMA
NAPA
YOLO
YUBA
SUTTER
SOLANO
MARIN
CONTRA COSTA
ALAMEDA
SACRAMENTO
SAN
MATEO
SANTA
CRUZ
SANTA CLARA
SAN JOAQUIN
STANISLAUS
CALAVERAS
TUOLUMNE
MONO
MERCED
MARIPOSA
MADERA
SAN BENITO
FRESNO
TULARE
INYO
SAN LUIS OBISPO
KERN
KINGS
SAN BERNARDINO
SANTA BARBARA
LOS
ANGELES
VENTURA
RIVERSIDE
IMPERIAL
SAN
DIEGO
ORANGE
MONTEREY
This map is based on a search of online available Codes and may have missed County other requirements such as non-codified requirements or requirements of city or regional agencies. This map presents findings for individual county requirements and deals only with the unincorporated areas of the counties, all area in California are subject to California and Federal biosolids regulations.
Notes: Bulleted Text Slide
Title: 40 pt Arial Bold, Flush Left
Content: 32 pt Arial, Flush Left
Bullets: Level 1 - Image “dropbullet.gif”; Level 2, 4 and 5 - Normal Text; Level 3 - Wingdings 2

## Slide 15: Biosolids Regulatory Foundation
USEPA adopted risk based federal standards for the use of biosolids in 1993 (40 CFR part 503) – replaced 40 CFR part 257 (which still regulates industrial residuals)
Biennial review required by CWA which has been done since 2003
SWRCB adopted Programmatic EIR and General Order in 2004
Biosolids are dually regulated by USEPA and SWRCB
Both regulatory frameworks promote the land application of biosolids
Two reviews by the NAS have supported the US regulations and land app

## Slide 16: Land application requires regulatory compliance with all of the following:
Pathogen control (Engineered process requirements) – Class A or Class B with Class B + management = Same level of safety as Class A
Biosolids cannot be a food source for disease carrying organisms – Vector Attraction Reduction required
Meet Pollutant Concentration limits set by comprehensive risk assessment conducted by USEPA
Limit the application rate of biosolids to the nitrogen need of crop to be grown (taking all N sources into account)

## Slide 17: Biosolids Regulatory Foundation
Regulation of biosolids is dynamic and must remain based on sound science
This is true for any regulation designed to protect public health and the environment and has been for biosolids since the CWA was adopted
An overarching finding of the NAS Committee in 2002, on which I served, was to continually pursue research – not because one would expect to find adverse impacts, but because it’s the responsible course of action
When evaluating new constituents, it is important to consider practical experience based on decades of land application and net environmental impacts

## Slide 18: BACKGROUND
On February 19, 1993, the final version of 40 CFR Part 503 biosolids rule was promulgated under the CWA and RCRA.
40 CFR Part 503 was designed to protect the public and environment from any reasonably anticipated adverse effects of recycled biosolids.

## Slide 19: 40 CFR Part 503 APPLIES TO…
Biosolids Generator (POTWs)
Mixtures (Composters, Regional facilities)
Land Application
  Contract appliers
  Reclamation (mines, superfund, fire impacted sites)
Surface Disposal
Incineration
Landfills (under 40 CFR part 258)

## Slide 20
TABLE A FREQUENCY OF MONITORING |  | 
Amount of Biosolids (Dry Metric Tons per 365 day) | Amount of Biosolids (Dry U.S. tons per 365) | Frequency
0 < X < 290 | 0 < 320 | Once per year
290 < = X < 1500 | 320 < = X < 1654 | Once per quarter
1500 < = X < 15000 | 1654 < = X < 16540 | Once per 60 days
15000 < = X | 16540 <= X | Once per month
1 Amount of biosolids land applied (dry weight basis). 2 Metric tons = U.S. tons x 0.907 |  | 

## Slide 21: Biosolids must meet all the following to be land applied (most restrictive in all three = Exceptional Quality)
METAL CONCENTRATIONS
  POLLUTANT LIMITS (HQ)
  CEILING LIMITS
PATHOGEN CONTROL
  CLASS A or
  CLASS B
VECTOR ATTRACTION REDUCTION
  PROCESS or
  PHYSICAL BARRIER

## Slide 22: USEPA Risk Assessment Process
Started with ~ 400 constituents
Narrowed to 200 on which a Hazard Index (HI) Assessment was performed
Full deterministic multi-pathway (14) risk assessment performed for 25 constituents with HI >1
Ultimately regulated 10 constituents in final rule
Biennial reviews continue to monitor new science and emerging constituents

## Slide 23: Highly Exposed Individual – Target of Risk Assessment
Is a home gardener who applies biosolids to the garden every year for 70 years and…
  Grows and consumes 60% of their food from their garden, consumes fish from a farm pond, drinks water from a private on-site well – all impacted by land application
  Home garden is at the maximum pollutant loading limit for all regulated constituents each year over the entire 70-year period
  45% home grown meat where livestock consume 100% of their feed from biosolids amended crops and 2.5% of their diet is dirt
  Food consumption was conservatively assumed based on Exposure Factors Handbook

## Slide 24: EPA Risk Assessment for Part 503: Exposure Pathways Assessed Agricultural Land Application Scenario to Assess Human Exposure
40+ Years of Research…
Risk Assessment
The presence of a contaminant in biosolids does not mean there is risk; its fate and impact on humans and the environment must be evaluated.
Notes: This is a pictorial display of the numerous input variables considered in a PRA. The Reasonable Maximum Exposure to an individual considers an entire range of exposures from multiple sources rather than a single discrete input point for each exposure pathway as is necessary in a deterministic risk assessment.

## Slide 25
METALS Land Application Pollutant Limits (all values are on a dry weight basis) |  |  |  | 
Pollutant | Ceiling Concentration Limits for All Biosolids Applied to Land (milligrams per kilogram) Table 1 | Cumulative Pollutant Loading Rate Limits for CPLR Biosolids (kilograms per hectare) Table 2 | “High Quality” Pollutant Concentration Limits (mg/kg) Table 3 | Annual Pollutant Loading Rate Limits for APLR Biosolids (kilograms per hectare per 365-day period) Table 4 (Obsolete)
Arsenic | 75 | 41 | 41 | 2.0
Cadmium | 85 | 39 | 39 | 1.9
Chromium | 3,000 | 1,200 | 3,000 | 150
Copper | 4,300 | 1,500 | 1,500 | 75
Lead | 840 | 300 | 300 | 15
Mercury | 57 | 17 | 17 | 0.85
Molybdenumb | 75 | - | - | -
Nickel | 420 | 420 | 420 | 21
Selenium | 100 | 36 100 | 36 100 | 5.0
Zinc | 7,500 | 2,800 | 2,800 | 140

## Slide 26: Pretreatment regulations have worked!
Pollutant concentrations in California are roughly an order of magnitude lower than the 503 limits
Pretreatment regulations implemented in late 1980’s and early 1990’s limited what industry could discharge to a POTW
Concentrations quickly dropped by about 1993 to best available control technology levels which are far below the risk based limits in part 503

## Slide 27: Some ‘Parts’ Math
100% = 1,000,000 mg/Kg (ppm)
10% = 100,000 mg/Kg (ppm)
1% = 10,000 mg/Kg (ppm)
1,000 mg/Kg or 1g/Kg = 1000ppm
1 mg/Kg =1 ppm
1 mg/Kg =0.001 ppm = 1 ppb
1 ng/Kg = 0.000001 ppm = 1 ppt
1 ppt – 1 second in ~ 32,000 years
Concentrations of chemicals in soil are typically measured in units of the mass of chemical (milligrams, mg or micrograms, ug) per mass of soil (kilogram, kg).
This is written as mg/kg or ug/kg. Sometimes concentrations in soil are reported as parts per million (ppm) or parts per billion (ppb).
For soil, 1 ppm = 1 mg/kg of contaminant in soil, and 1 ppb = 1 ug/kg. A measurement of 6 mg/kg is the same as 6 ppm or 6,000 ppb, which is equal to 6,000 ug/kg.
Notes: One part per million (ppm) denotes one part per 1,000,000 parts, one part in 106, and a value of 1 × 10–6. This is equivalent to one drop of water diluted into 50 liters (roughly the fuel tank capacity of a compact car), or about thirty seconds out of a year.
One part per billion (ppb) denotes one part per 1,000,000,000 parts, one part in 109, and a value of 1 × 10–9. This is equivalent to 1 drop of water diluted into 250 chemical drums (50 m3), or about three seconds out of a century.
One part per trillion (ppt) denotes one part per 1,000,000,000,000 parts, one part in 1012, and a value of 1 × 10–12. This is equivalent to 1 drop of water diluted into 20, two-meter-deep Olympic-size swimming pools (50,000 m3), or about three seconds out of every hundred thousand years.
One part per quadrillion (ppq) denotes one part per 1,000,000,000,000,000 parts, one part in 1015, and a value of 1 × 10–15. This is equivalent to 1 drop of water diluted into a cube of water measuring approximately 368 meters on a side (fifty million cubic meters, which is a cube about as tall as the roof of the Empire State Building), or two and a half minutes out of the age of the Earth (4.5 billion years). Although relatively uncommon in analytic chemistry, measurements at the ppq level are performed.[4]

## Slide 28: Pathogens Must be Reduced
Class A requires Process to Further Reduce Pathogens (PFRP) which produces a non-detect level for pathogens
Class B requires Process to Significantly Reduce Pathogens (PSRP)
Class B + Management practices (which allow for natural attenuation) = same level of protection as Class A

## Slide 29
CLASS A |  | 
PARAMETER | UNIT | LIMIT
Fecal Coliform or Salmonella | MPN/g TS | 1000
 | MPN/4g TS | 3
AND, ONE OF THE FOLLOWING PFRP PROCESS OPTIONS |  | 
Temp/Time based on % Solids | Alkaline Treatment | 
Prior test for Enteric Virus/Viable Helminth Ova | Post test for Enteric Virus/Viable Helminth Ova | 
Composting | Heat Drying | 
Heat Treatment | Thermophilic Aerobic Digestion | 
Beta Ray Irradiation | Gamma Ray Irradiation | 
Pasteurization | PFRP Equivalent Process | 

## Slide 30
CLASS B |  | 
PARAMETER | UNIT | LIMIT
Fecal Coliform | MPN or CFU/gTS | 2,000,000
OR ONE OF THE FOLLOWING PSRP PROCESS OPTIONS |  | 
Aerobic Digestion | Air Drying | 
Anerobic Digestion | Composting | 
Alkaline Stabilization | PSRP Equivalent | 

## Slide 31: Vector Attraction Reduction (VAR)
Biosolids must not be an attractive food source to vectors (birds, rodents, insects, etc.) which are capable of transporting pathogens off-site
10 options are offered to meet the requirement
First 5 can be met following treatment and last 5 must be met when land applied

## Slide 32
TABLE 7 VECTOR ATTRACTION REDUCTION (One of the following must be satisfied) |  | 
OPTION | LIMIT | WHERE IT MUST BE MET
Volatile Solids Reduction | >38% | Across the process
Specific Oxygen Uptake Rate | <1.5mg O2/hr/g TS | On aerobic stabilized sludge
Anaerobic bench-scale test | <17& VS reduction | On anaerobic digested sludge
Aerobic bench-scale test | <15% VS reduction | On aerobic digested sludge
Aerobic Process | >14 days, T>40° C and avg T >45° C | On composted sludge

## Slide 33
TABLE 7 VECTOR ATTRACTION REDUCTION |  | 
OPTION | LIMIT | WHERE IT MUST BE MET
pH adjustment | >12 S.U. (for 2 hours) and >11.5 (for an additional 22 hours) | When applied or bagged
Drying without primary solids | >75% TS | When applied or bagged
Drying with primary solids | >90% TS | When applied or bagged
Injection | - | When applied
Incorporation | - | When applied

## Slide 34: NUTRIENT MGMT
Application is limited to the nitrogen needs of the crop during the season for it to be grown – minimize leaching potential
Since most N in biosolids is organic, it is slowly mineralized and becomes available as the crop needs it
All sources of nitrogen must be taken into account (manure, commercial fertilizer, carry over from previous biosolids application) when setting application rate

## Slide 35: Land Application Restrictions for Class B Biosolids
Must not Endanger Threatened or Endangered Species
Must not Disturb Historical Properties
Soil pH > 5.5
At least 10 meters from surface water/wetlands
Must meet Table C Time Requirements

## Slide 36
TABLE C MINIMUM DURATION BETWEEN APPLICATION AND HARVEST\GRAZING\ACCESS FOR CLASS B BIOSOLIDS APPLIED TO THE LAND |  |  | 
Criteria | Surface | Incorporation | Injection
Food crops whose harvested part may touch the soil/biosolids mixture (beans, melons, squash, etc.) | 14 months | 14 months | 14 months
Food crops whose harvested parts grow in the soil (potatoes, carrots, etc.) | 20/28 months* | 20/38 months* | 38 months
Feed or other food crops (field corn, hay sweet corn, etc.) | 30 days | 30 days | 30 days
Grazing of animals | 30 days | 30 days | 30 days
Public access restriction |  |  | 
High potential | 1 year | 1 year | 1 year
Low potential | 30 days | 30 days | 30 days
*The 20 month duration between application and harvesting applies when the surface applied biosolids stays on the surface for 4 months or longer prior to incorporation. The 38 month duration is in effect when the biosolids remains on the surface for less than 4 months prior to incorporation. |  |  | 

## Slide 37: Recommended Changes to Biosolids General Order
Remove ability for local jurisdictions to be more restrictive
Do not use background soil concentrations as part of the cumulative soil limit since they were included in the risk assessment
Adopt the federal restriction for animal grazing after application (30 days)
Do not apply the GO to exceptional quality biosolids
Delete remanded limit for Molybdenum

## Slide 38
LOCAL PROBLEM SOLVED BY LOCAL STUDY
January 2020 – Pima County (Tuscon, AZ) Board of Supervisors impose moratorium on land application in Pima County
March – October 2020 – University of Arizona Water and Environmental Technology Center (WET) in collaboration with Pima County Wastewater evaluate incidence and transport of PFAS following long-term land application (since 1984)
Data showed low incidence of soil PFAS and limited mobility of PFAS through soil and vadose zone
Data presented to Pima County Administrator
December 2020, moratorium rescinded
FOR A NATIONAL PROBLEM WE NEED A NATIONAL STUDY

## Slide 39
EVALUATION OF FATE AND TRANSPORT OF PFAS FOLLOWING LONG-TERM LAND APPLICATION: A COLLABORATIVE NATIONAL STUDY
Principal Investigator: Ian Pepper
University of Arizona
Co-Principal Investigators: Mark Brusseau
University of Arizona
Greg Kester
California Association of Sanitation Agencies
Jeff Prevatt
Pima County Wastewater

## Slide 40
NATIONAL COLLABORATIVE PROJECT
OVERALL PROJECT GOAL
To evaluate whether or not land application of biosolids is a significant public health route of exposure to perfluorinated compounds (PFAS)
Specific Objectives:
Evaluate
Incidence of PFAS analytes in soil following long-term land application of biosolids
Mobility (leaching) of PFAS analytes through soil and vadose zone under the influence of rainfall and/or irrigation
Crop uptake of PFAS analytes

## Slide 41: EPA Office of Inspector General Report
Released in November 2018 – Viewed as sensational indictment of EPA biosolids program
Implied land application is unsafe until full risk assessment is conducted on 352 constituents
CASA began working with Universities (U of AZ, Ohio State, Purdue) to rebut report conclusions
Submitted formal response July 2020 as product of USDA W4170 Multi-state research committee

## Slide 42: Rebuttal Summary and Conclusions
Extensive data and risk assessment for many of the chemicals in the OIG report.
Lack of consideration by OIG of low concentration of chemicals of concern in biosolids OIG report
Low concentration of most chemicals causes little exposure and risk
Most chemicals in biosolids were (i) below natural soil levels, (ii) non toxic and pose no risk, (iii) result in minimal exposure and risk, or (iv) will not persist in the environment
Due to sorption and degradation, antibiotic activity does not build up in soil despite natural production by soil microbes and anthropogenic inputs
Natural production of antibiotics in soil has occurred for billions of years
PFAS are currently under study

## Slide 43: Benefits of Biosolids in California
Land application of biosolids provides all the following:
  Improves soil tilth, increasing soil organic carbon
  Increases water holding capacity, reducing irrigation demand
  Reduces crop drought stress
  Increases crop yields
  Sequesters carbon long-term
  Displaces fossil fuel-intense inorganic fertilizer (0.22 gallons of fossil fuel needed for every pound of inorganic nitrogen)
  Conserves non-renewable resources (like phosphorus) and recycles them
  Can help reclaim disturbed sites such as superfund and other mines, brownfields, and fire-impacted land
Without biosolids
Adjacent field amended with biosolids

## Slide 44: Biosolids are a resource that have been documented to improve the environment in several ways
Biosolids improve soil fertility
Portion of field that has not received biosolids
Portion of same field that has received biosolids

## Slide 45: Research and Safe Practices of Biosolids
Not One Documented Adverse Effect of Biosolids Application Over Decades
Research has Been Done Over the Past 70 Years with Universal Support of Land Application as the most Sustainable and Beneficial Use
Research and Risk Assessment Continue for Emerging Contaminants of Concern
EPA Recently Updated its Biosolids Screening and Full Risk Assessment Models
Science Advisory Board is reviewing them and convened an expert Biosolids panel, to which I have been appointed

## Slide 46
We are public agencies that work to serve the public good
California agencies follow all existing regulations.
Research and experience have demonstrated numerous benefits from using biosolids.
There has not been any documented negative impacts to human health from the use of biosolids as a fertilizer.
Our agencies are eager to work with regulators to answer any questions they have with research studies led by independent University of California researchers or other academic institutions.

## Slide 47: Questions?
Greg Kester
CASA Director of Renewable Resource Programs
gkester@casaweb.org
916-844-5262