## Slide 1: What can we learn from the GeoTracker PFAS data?
Chris Gurr, PE
CDM Smith
April 26, 2022

## Slide 2: Experimental Methods & Provisional Data Quality
40 CFR 136 / USEPA
Experimental, non-approved methods
Frequency of Non-detects
USEPA guidance indicates that monitoring should not be commenced or required until after a multi- lab validated method is made available to the public. In addition, USEPA’s criteria for certifying a new standard method requires a thorough demonstration of accuracy, precision, representativeness, ruggedness, and comparability. Because no USEPA certified or approved standard analytical test method currently exists for PFAS in non-potable water [and/or solid matrices], the data submitted herein should be considered as provisional.
The data is not intended for any regulatory purpose other than in response to the State Water Board’s Order, and should not be used for any other compliance or regulatory purpose under any statutory or regulatory scheme, including, but not limited to the federal Clean Water Act, the Safe Drinking Water Act, and/or the Porter- Cologne Water Quality Control Act.

## Slide 5
Chemical | ChainType | Subclass | Chain Length
PFBA | Short Chain | PFCA | C004
PFPeA | Short Chain | PFCA | C005
PFHxA | Short Chain | PFCA | C006
PFHpA | Short Chain | PFCA | C007
PFOA | Long Chain | PFCA | C008
PFNA | Long Chain | PFCA | C009
PFDA | Long Chain | PFCA | C010
PFUnDA | Long Chain | PFCA | C011
PFDoDA | Long Chain | PFCA | C012
PFTrDA | Long Chain | PFCA | C013
PRTeDA | Long Chain | PFCA | C014
PFHxDA | Long Chain | PFCA | C016
PFODA | Long Chain | PFCA | C018
3:3FTCA | Short Chain | PFCA- Precursor | Short Chain
4:2FTS | Short Chain | PFCA- Precursor | Short Chain
5:3FTCA | Short Chain | PFCA- Precursor | Short Chain
6:2FTS | Short Chain | PFCA- Precursor | Short Chain
7:3FTCA | Long Chain | PFCA- Precursor | Long Chain
8:2FTS | Long Chain | PFCA- Precursor | Long Chain
10:2FTS | Long Chain | PFCA- Precursor | Long Chain
10:2FTS | Long Chain | PFCA- Precursor | Long Chain
Chemical | ChainType | Subclass | Chain Length
PFBS | Short Chain | PFSA | C004
PFPeS | Short Chain | PFSA | C005
PFHxS | Short Chain | PFSA | C006
PFHpS | Long Chain | PFSA | C007
PFOS | Long Chain | PFSA | C008
PFNS | Long Chain | PFSA | C009
PFDS | Long Chain | PFSA | C010
PFDOS | Long Chain | PFSA | C012
ETFOSA | Long Chain | PFSA- Precursor | Long Chain
ETFOSE | Long Chain | PFSA- Precursor | Long Chain
MEFOSA | Long Chain | PFSA- Precursor | Long Chain
MEFOSE | Long Chain | PFSA- Precursor | Long Chain
NETFOSAA | Long Chain | PFSA- Precursor | Long Chain
NMEFOSAA | Long Chain | PFSA- Precursor | Long Chain
PFOSA | Long Chain | PFSA- Precursor | Long Chain
11ClPF3OUDS | Long Chain | Per or Polyfluoroether | Long Chain
9ClPF3ONS | Long Chain | Per or Polyfluoroether | Long Chain
ADONA | Long Chain | Per or Polyfluoroether | Long Chain
HFPO-DA | Long Chain | Per or Polyfluoroether | Long Chain
HFPO-DA | Long Chain | Per or Polyfluoroether | Long Chain
Alphabet Soup

## Slide 6: Research Questions
What is a PFAS “baseline” for POTWs?
Do industrial discharges create PFAS above baseline?
Are there PFAS signatures of industrial point sources?
Where are the “outliers”?
What are the blind spots or major uncertainties in the dataset?

## Slide 7: POTWs Distribution by Residential & Commercial Contribution
Total of 272 facilities
80% < 10% Industrial Contribution

## Slide 8: Research Questions
What is a PFAS “baseline” for POTWs?
Do industrial discharges create PFAS above baseline?
Are there PFAS signatures of industrial point sources?
Where are the “outliers”?
What are the blind spots or major uncertainties in the dataset?

## Slide 9
Wastestream PFAS Profile by Residential & Commercial Contribution

## Slide 11: Sensitivity to NDs Quantification
Examples: 3 approaches handling NDs when calculating ∑quantified PFAS
“As-reported” = use values as shown on the GeoTracker. Depending on the laboratory performing the analysis, some NDs were reported as 0, some as the Detection Limit.
“Full detection limit” = values for NDs are substituted with the Detection Limit reported by the laboratory.
“Non-detect to 0” = All NDs treated as 0 nanograms per Liter (liquids) or micrograms per kilogram (solids)
State-wide samples
POTWs with 100% residential & commercial flow

## Slide 12: Analyte Median Sensitivity to NDs Quantification
Analyte | Group | Percent of samples with Reporting Limits less than the Order requirements (%) | Median Concentration (ppt) |  | 
Analyte |  | % reporting limit (i.e. how confident are we in this concentration) | As-reported | Full detection limit | Non-detects to 0
PFBS | PFSA / Short Chain | 42 | 2.03 | 5 | 0
PFHxS | PFSA / Short Chain | 42 | 1.9 | 5 | 0
PFOS | PFSA / Long Chain | 42 | 2.64 | 5 | 0
PFHxA | PFCA / Short Chain | 50 | 6.64 | 8.6 | 3.88
PFHpA | PFCA / Short Chain | 41 | 1.81 | 5 | 0
PFOA | PFCA / Long Chain | 41 | 3.23 | 7.7 | 0
PFNA | PFCA / Long Chain | 41 | 0.9 | 4.66 | 0
PFDA | PFCA / Long Chain | 41 | 1 | 4.9 | 0
ADONA | Per or Polyfluoroether / Long Chain | 43 | 0.35 | 5 | 0
Influent samples
All POTWs

## Slide 13: With so many NDs, how can we leverage distributions for PFAS rather than summary statistics?

## Slide 14: Research Questions
What is a PFAS “baseline” for POTWs?
Do industrial discharges create PFAS above baseline?
Are there PFAS signatures of industrial point sources?
Where are the “outliers”?
What are the blind spots or major uncertainties in the dataset?

## Slide 15: We Used Questionnaire Answers to Group POTWs

## Slide 16: Detections Ranked from Low Concentration to High

## Slide 17
Detections Ranked from Low Concentration to High
Influent

## Slide 18
Detections Ranked from Low Concentration to High
Effluent

## Slide 19
Detections Ranked from Low Concentration to High
Biosolids

## Slide 20: Research Questions
What is a PFAS “baseline” for POTWs?
Do industrial discharges create PFAS above baseline?
Are there PFAS signatures of industrial point sources?
Where are the “outliers”?
What are the blind spots or major uncertainties in the dataset?

## Slide 21: “Outlier” POTWs are visible in the data
State-wide samples
POTWs with 100% residential & commercial flow
∑quantified PFAS for each sample
“Non-detect to 0” case
Preliminary

## Slide 22
Detections Only
Influent

## Slide 23
Detections Only
Effluent

## Slide 24
Detections Only
Biosolids

## Slide 25: Research Questions
What is a PFAS “baseline” for POTWs?
Do industrial discharges create PFAS above baseline?
Are there PFAS signatures of industrial point sources?
Where are the “outliers”?
What are the blind spots or major uncertainties in the dataset?

## Slide 26: Uncertainties and Blind Spots
NDs need to be handled with care
Wastewater is a complex matrix. Difficult to analyze chemically.

## Slide 27
We continue to work on:
Outliers
Signatures of industrial contributions
Signatures of residential contributions
WRF 5031, Occurrence of PFAS in US Wastewater Treatment Plants

## Slide 28: Thank you Chris Gurr, PE gurrc@cdmsmith.com