## Slide 1: WELCOME TO BERKELEY June 3, 2025

## Slide 2: Thank you to our supporters
Brown & Caldwell
Cambi, Inc
Carollo Engineers
Carpinteria Sanitary District
City of Richmond
Coombs Hopkins
Dudek
GHD
Hazen & Sawyer
HDR Engineering
Jacobs
Lystek
South Orange County WA
Synagro
Unisense Environment
West Yost Associates
Woodard & Curran
Notes: Carp San

## Slide 3: Thank you to our sponsors

## Slide 4
READY
IN 1-2
WEEKS
CONTACT HOURS
FOR TODAY’S EVENT
AUTOMATED
Notes: A note about contact hour process…
Member Services will use the sign-in sheet from today’s event and move your contact hours over to your CWEA member record.
If you hold a CWEA certification, nothing further is required.
The contact hours are in the system and will be applied to your certification.

## Slide 5: WELCOME TO BERKELEY June 3, 2025

## Slide 6
Innovation in Wastewater Policy
Felicia Marcus
William C. Landreth Visiting Fellow
Water in the West
Stanford University

## Slide 7
Reverse Osmosis Concentrate Management ANGELA STEIGLER, MODERATOR
Hazen

## Slide 8: Reverse Osmosis (RO) is the leading technology for potable reuse of municipal wastewater
Feed
Concentrate
15% of flow
Permeate
85% of flow
Reverse osmosis
Modified from Finnerty et al. 2023
Discharge
Treatment or Volume Reduction

## Slide 9: Municipal Wastewater RO Concentrate Management Perspectives
RO maximizes possible uses for alternative water supplies
Incentive to maximize recoveries
RO permeate represents a PFAS-free water supply
Water Supply
Wastewater Treatment
Loads remain the same, concentrations are 5-6x higher
Opportunity to manage contaminants in a smaller flow/volume
Few MWRC treatability studies
Pressure from emerging regulations

## Slide 10: Partnering for Impact on MWROC Management
MWROC management requires collaboration and partnership
Opportunities for research and innovation to:
  Reduce costs
  Maximize benefits
  Meet regulatory goals
Modified from Finnerty et al. 2023

## Slide 11: Our Panelists
Alternative Water Supply Program Manager
SFPUC
Professor of Civil & Environmental Engineering;
Director of the Berkeley Water Center
UC Berkeley
North American Water Treatment and Desalination Lead
GHD
Manisha Kothari
David Sedlak
Mark Donovan

## Slide 12
Roundtable Discussions

## Slide 13
Nutrient Removal – Energy Emissions Nexus SARAH DESLAURIERS, MODERATOR
CASA
Notes: As the State Water Board continues their work on its statewide nutrient strategy and various Regional Water Boards seek to further limit nutrients in WWTP effluent, we must take a step back to look at the bigger picture – how are we impacting the nitrogen cycle? How much energy is required? How much supplemental carbon is needed? What types of emissions (including nitrous oxide) will this lead to? This panel will dive into the drivers of nutrient removal, treatment options, and what we need to know to optimize treatment and emissions.

## Slide 14: Nutrients in Wastewater
Notes: Triethanolamine in many personal care products

## Slide 15: Wastewater Treatment Removes Nutrients to Protect Receiving Waters
Treatment needs vary from plant to plant
Treatment operations can be energy-intensive
Treatment may require chemical addition (chemical production can be energy-intensive)
Integrating new technology must look at up- and down-stream impacts
Increased intensity of treatment or changes to operations to enhance nutrient removal can lead to increased emissions
Must look at the big picture to understand net impact
Notes: Will mention that aeration typically accounts for 40-60% of the energy demand and the energy demand typically represents the larger portion of a WWTP GHG inventory.
Will make reference to Mike Falk and Krishna Pagilla work.

## Slide 16: Optimize Nutrient Removal, Energy, & Emissions!
Nutrient removal is a top priority for the State and Regional Water Boards
Carbon neutrality is a top priority for the Air Resources Board
National research has been underway for decades on each topic
California and Denmark have a partnership to share information on the water-energy-emissions nexus work at Aarhus Vand (and others)
CASA Research Collaborative is working to bring partners together in CA
Notes: Will make reference to Aarhus Vand and DHI working partnership.

## Slide 17
Approaches to Nutrient Removal
HDR
Nitrogen Removal Treatment – Energy & Nitrous Oxide Emissions,
University of Nevada - Reno
Monitoring Nitrogen Removal for Performance Optimization at Aarhus Vand (Denmark) & Utilizing Data through Digital Twin Modeling,
DHI
Dr. Mike Falk
Dr. Krishna Pagilla
Christophe Boisvert
Our Panelists
Notes: Sarah to provide a few questions to the panelists 5/30.

## Slide 18
Impairment of Aesthetics, Recreation, Aquatic Life, and Water Supply
Strategic to “squeeze THE pipes” more effectively

## Slide 19: Drivers Specific to California
Algae Blooms (Freshwater and Brackish)
  Bay Area: 2022/2023
  SoCal Bight
  Freshwater
Ocean Acidification (related to Algae)
Depressed Dissolved Oxygen Levels
Public Health: Blue-Baby Syndrome
Freshwater Mussels
Others

## Slide 20: On-Going and Future Treatment Themes
Treatment and Process (How to “Squeeze” More Out of the Pipes):
  Optimization
  Sidestream Treatment
  Upgrades
  Process Intensification
  Resource Recovery
Supply/Reuse: Potable Reuse (refer to Reverse Osmosis Conc Challenges Discussion)
By Other Means: Reuse, Nature-based Solutions, etc.
Non-Point Source Loads: Agriculture, Stormwater, etc.

## Slide 21: Blueprint for Regional Approaches : Holistic Approach to Improved Nutrient Management: Phase 1 WRF #4974
Holistic Approach to Improved Nutrient Management | The Water Research Foundation (waterrf.org)

## Slide 22: Holistic Pollution Management: Practices, Policies, and Partnerships (3 P’s)
Key Factors Influencing Holistic Nutrient Mgmt
Practices
  Treatment
  Best Management Practices
Policies
  Regulatory Frameworks
  Watershed Governance
Partnerships
  Collaboration
  Leadership
Notes: I’ll use the Framework we developed for the Water Research Foundation project WRF4974 to provide the 3P’s of Practices, Policies and Partnerships

## Slide 23: Regional Approaches: Balance the 3 P’s to Incentivize Cost-Effective and Beneficial Regional Solutions

## Slide 24
Nitrous Oxide Emissions from WRFs during N Removal
Krishna Pagilla, PhD, PE, BCEE
Ralph & Rose Hoeper Endowed Professor
Director, Nevada Water Innovation Institute
Notes: 24

## Slide 25: Nitrous Oxide (N2O) Emissions and Aeration Energy in N Removal
N2O is emitted from:
  Biological N Removal Process
  Secondary Treatment
  Discharged Effluent
Overall WRF Carbon Footprint
  >50% Energy for Aeration (Scope 2)
  Nitrification Doubles Aeration Demand
  Sidestream Treatment Increases Energy Demand

## Slide 26: Possible Nitrous Oxide (N2O) Pathways
Influencing Factors:
  High NH4-N and High NO2-N in Nitrification
  Low DO, High NO2-N, and NH4-N Availability in Autotrophic Denitrification
  High DO, High NO2-N, BOD/COD Limitation in Heterotrophic Denitrification
Ref. STOWA 2011

## Slide 27
N2O Emissions from Activated Sludge (Ahn et al., 2010. EST; Ahn et al., 2010, WER; Rassamee et al., 2011, B&B)
National Study Funded by Water Environment Research Foundation (WERF U4R07; 2008-2009)
  More N2O emissions observed from aerobic vs anoxic conditions
  High variability across WRFs and diurnally within each WRF
  Single emission factor for all WRFs is not appropriate
  High Nitrite, Ammonium, and DO concentrations were positively correlated to N2O Emissions; other factors may play an indirect role
  BNR processes that minimize transient conditions and achieve complete N removal (low TN effluents) are likely to have lower N2O emissions
  More facility-level research needed

## Slide 28
Key Findings from Recent Work* (2024)
  *Oversimplification and Mis-estimation of Nitrous Oxide Emissions from Wastewater Treatment Plants, 2024 – Cuihong Song, Jun-Jie Zhu, John Willis, Daniel Moore, Mark Zondlo, Zhiyong Jason Ren, Nature Sustainability
  The results reveal the diverse nature of wastewater N2O emissions and underscore the need for a customized approach to inform facility-level N2O emission estimation as well as inform national- and sector-wide GHG inventories with emphasis on site-specific considerations.

## Slide 29: Key Insights
  BNR at WRFs emit N2O at various levels – Variability is common!
  Need facility-level approach for accurate estimation and N-removal process selection
  Many process factors (temperature, DO, pH, ammonium levels, C/N Ratio, aeration rate/type, and transient conditions) are responsible – DO and Transient Conditions are dominant factors for N2O emissions
  Low TN plants have lower risk of N2O emissions
  Understanding N2O emissions at a facility is directly related to understanding the BNR operations and performance
  N2O emissions in WRFs may constitute majority of total direct (Scope 1) GHG emissions if not optimized

## Slide 30
Christophe Boisvert, DHI
Carles Pellicer-Nàcher, F. Polesel, M. Rebsdorf, A. Lynggaard-Jensen, E. Brodersen, M. Guldborg Hansen, P. Andreasen, T. Dalkvist
Predicting And Mitigating N2O Emissions In WWTPs Can Digital Twins Help Achieve Carbon Neutrality?

## Slide 31: Digital twins: why?
Benefits in the context of N2O mitigation:
  Analyse and contextualize complex N2O process data
  Soft sensoring to decipher N2O production mechanisms
  From data to action – mitigation of N2O emissions
Source: https://albertawater.com/influences/wastewater-treatment-plants/
Source: https://www.controleng.com/articles/digital-twin-improves-plant-design-and-operational-performance/
Source: https://www.forecastr.co/blog/time-series-forecasting-model

## Slide 32: Calibration - (Marselisborg, batch mode pilot plant)
No significant abiotic N2O production
N2O Dosing (anx)
NO3- Dosing (anx)
NH4+ dosing (aer/anx)
Aeration on
Aeration off

## Slide 33: Validation – full scale WWTP (Bjergmarken)
Controllers
Aeration:
  Alternating inlet/outlet and N/DN
  Ammonia-based DO set-point
RAS recirculation
Sludge wastage
Inputs to the model
Flow
Temperature
Influent fractionation from historical lab data
RAS flows
3-digits phase codes for alternating N/DN
Sensors in PTs
NH4+, NO3-
N2O liquid phase
DO
TP/PO4-
MLSS
Notes: Capacity: 125,000 PE
No primary settler
Biological treatment: Biodenipho
  Pre-anaerobic tank
  Alternating anoxic-aerobic tanks (4 + 2 tanks)
Secondary settlers
Longitudinal secondary settlers (9x)
Sidestream hydrolysis (SSH) of settled sludge
Anaerobic digestion and sludge dewatering

## Slide 34: Modelled vs. Measured N2O Concentrations
EFN2O = 1.3% kg N2O-N/kg N
Process Tank 2 – N2O
Process Tank 3 – N2O

## Slide 35: Scenario Analysis (offline WEST modeling)
Pairing of measured data with N2O (liquid phase)

## Slide 36
Roundtable Discussions

## Slide 37
Q&A

## Slide 38
Call to Action
Felicia Marcus
William C. Landreth Visiting Fellow
Water in the West
Stanford University

## Slide 39: Thank you to our sponsors

## Slide 40: THANK YOU

## Slide 41: Attendee Happy Hour Meet-up
DAVID BROWER CENTER Terrace 2181 Shattuck Ave
Berkeley